## Slide 1
Urban Traffic State Estimation by Fusing Multisource Information

## Slide 2: Data fusion is important
Problem:
Difficult to provide complete and accurate traffic information just using one single data source
Each source of data (e.g. GPS location data, traffic cameras) has benefits and drawbacks, e.g. sparseness, error rate
Potential Applications:
Traffic management software to guide travelers
Validation of traffic simulations
Draw conclusions about relevance of fused datasets

## Slide 3: Datasets Used For Traffic State Estimation
Dataset | Nature | Comments
Traffic Images | Real time | Use images provided by the LTA data-mall API to count the number of cars which is used as means to derive traffic density.
Floating car data | Historic | 100 million map-matched data points providing the following information. road-id, latitude, longitude, speed, time-stamp.
Loop detector data | Historic | Use loop detector data from several intersections which provide information on traffic flow and occupancy.
Traffic speed band | Real time | Traffic speed band data from the LTA data mall API.
eZLink | Historic | Data collected from eZLink smart cards providing service line, ride distance and travel time in buses.
Notes: Mention lta dataMall

## Slide 4
DataMall camera locations on
Singapore expressways
Notes: 78 cameras
17 on PIE
Focus on 3

## Slide 6
Cameras suitable for visual analytics

## Slide 7
Difficult to analyze visually

## Slide 8
Detecting vehicles using HAAR features*
Apply Haar-feature to every input image
This results in a lot of features (>100000)
Use Adaboost to select the best features
* Rapid Object Detection using a Boosted Cascade of Simple Features, Paul Viola & Michael Jones, 2001

## Slide 9: Positive Clipped Images

## Slide 10: Negative Clipped Images

## Slide 11: Saving road data for each camera
Mask as an array of points
Number of Lanes
Length of the lane
Save for each region of interest:

## Slide 12: Adam Road (Cam ID: 6705)

## Slide 13: Bukit Timah Expressway (Cam ID 6706)

## Slide 14: Entrance from Jalan Anak Bukit (Cam ID 6710)

## Slide 15
Traffic densities for P.I.E. camera ID 6705

## Slide 16
From density to speed
V = vf * exp(-0.07016 * k^0.75)
Study conducted on Singapore’s linked
arterial roads suggests*:
Some models proposed in literature:
*Speed-flow modeling of arterial roads in Singapore. Lum at al., 1998
V: speed
vf: free flow speed calculated from QI
k: traffic density

## Slide 17
Connecting datasets:
Mapping of camera ID to road ID

## Slide 18
DataMall camera locations on Singapore expressways

## Slide 19
System used in Singapore:
SCATS (Sydney Coordinated Adaptive
Traffic System)
Implemented at intersections
Developed for over 40 years
Sold to 27 countries
Loop detector data

## Slide 20: Loop detector data collection
Gather data from ~300 intersections
which are classified as major in the
QI dataset
Obtain vehicle counts in 5 minute
intervals for each loop detector
Data collected in collaboration with
the LTA over the course of a week
Report of SCATS counts for 1 detector on 1 lane.
Columns refer to hour of day, rows to minutes.

## Slide 22: Loop Detector Images

## Slide 23
BPR formula:
Vr is the observed average speed on link r
VFr is the velocity in free flow conditions on link r
From vehicle counts to mean speeds
Notes: α represents the ratio between free flow speed and speed at capacity
β determines how steeply the curve bends once the capacity is reached
γ captures the effect of speed reduction due to opposite traffic in roads with non-separated lanes

## Slide 24: Quantum Inventions (QI) dataset specifications
GPS location data
9 weeks between 1st August 2014 and 1st October 2014
~ 100 million speeds extracted after map matching
Median ~25 seconds between consecutive timestamps
Form of data: (trackID, timestamp,
location, speed)

## Slide 25: QI traffic state

## Slide 27: Comparison of datasets
So far: speed extracted from every dataset
Now: compare different datasets:
  Loop with QI on major roads
  Camera with QI on expressways
Method: accumulate all data points for QI and loop detector and the last ~8 weeks for cameras in 15 minute intervals on given QI road segments and assume there is one traffic state

## Slide 28
Comparison: camera - QI

## Slide 29: Jurong West Ave 2 x Coorporation Rd

## Slide 30: Correlation between QI and LOOP
Investigating uncertainty in BPR formula parameters The Næstved model case study
α = 4.0
β = 1.8

## Slide 31: Use eZLink data for parameter estimation
Travel times and distances of buses can be derived from eZLink smart card data from 2013
Focus on bus service lines where there are a lot of QI and camera/loop detector data points
Concentrate on bus stops that are far apart to be sure the bus flows within the traffic
Service line 151

## Slide 32: Data fusion workflow
A Fusion-Based System for Road-Network Traffic State Surveillance: A Case Study of Shanghai

## Slide 33: Kalman filtering to reduce noise in data
The speeds we get from each data source are noisy!
Use Kalman filter to estimate the state of a discrete time controlled process

## Slide 34: Data fusion workflow
A Fusion-Based System for Road-Network Traffic State Surveillance: A Case Study of Shanghai

## Slide 35: Use Dempster Shafer Theory to fuse data
Goal: combine speeds (Loop detector, camera, QI) to estimate traffic state
DS – Theory provides a way to fuse floating point mean speeds into a set of
discrete traffic states
I use it as follows: aggregate all QI, Loop and camera speed data points on weekdays in 15 minute time intervals, smooth, fuse smoothed speeds to a discrete traffic state

## Slide 36: QI - distribution of data points 14:00 – 14:15, Cam ID 6705

## Slide 37
Camera - distribution of data points
14:00 – 14:15, Cam ID 6705

## Slide 38: Example
A murder has been committed. There are three suspects: Ω = {Peter, John, Mary}.
A witness saw the murderer going away in the dark, and he can only assert that it was man. How, we know that the witness is drunk 20 % of the time.
This piece of evidence can be represented by
    m({Peter, John}) = 0.8,
    m(Ω) = 0.2
The mass 0.2 is not committed to {Mary}, because the
testimony does not accuse Mary at all!
DS- Theory Similar to probability theory but
incorporates the concept of ignorance

## Slide 39: Practical Example for DS Combination
Every speed value gets assigned a certain mass (“probability”)
Fuse those masses according to rules provided by the theory

## Slide 40
Fusion results in final state S4

## Slide 41: Future work
Extract Parameters from eZLink dataset
Validation of fusion using traffic cameras and traffic speed band data
Estimation of the reliability of datasets in DS – theory
Validation of CityMOS

## Slide 42: Relevant literature
A Fusion-Based System for Road—Network Traffic State Surveillance: A Case Study of Shanghai, Qing-Jie Kong et al.
An Approach to Urban Traffic State Estimation by
Fusing Multisource Information, Zhipeng Li at al.